## Slide 1: CSCI 210
Chapter 1 Homework Assignment
Fall 2023
Dr. Jones – 210 Section 01
<YOUR NAME HERE>

## Slide 2: Instructions
Complete all these problems electronically (or hand-write them, will ALL work, and do so neatly, and paste in cropped scanned images in between each problem). – Using this PPT as a starting place
Exercises 1.15.1 – 1.15.11 (so 11 problems in total – with all sub problems).
Paste in the questions themselves into document too, like this (for 1.15.4 as an example)

## Slide 3: Question: 1.15.4
Start putting your work here, solution. Show all steps and all details – err on the side of too much detail rather than not enough.

## Slide 4: Submission
Submit this completed PPT into Moodle.

## Slide 5: List and describe three types of computers.
A personal computer (PC) is a computer designed for use by an individual, usually incorporating a graphics display, a keyboard, and a mouse.
An embedded computer is a computer inside another device used for running one predetermined application or collection of software.
A server is a computer used for running larger programs for multiple users, often simultaneously, and typically accessed only via a network.

## Slide 6: The seven great ideas in computer architecture are similar to ideas from other fields. Match the seven ideas from computer architecture, "Use Abstraction to Simplify Design", "Make the Common Case Fast", "Performance via Parallelism", "Performance via Pipelining", "Performance via Prediction", "Hierarchy of Memories", and "Dependability via Redundancy" to the following ideas from other fields: Assembly lines in automobile manufacturing - Performance via pipelining Suspension bridge cables - Performance via parallelism Aircraft and marine navigation systems that incorporate wind information - Performance via Prediction Express elevators in buildings - Make the common case fast Library reserve desk - Hierarchy of memories Increasing the gate area on a CMOS transistor to decrease its switching time - Dependability via redundancy Building self-driving cars whose control systems partially rely on existing sensor systems already installed into the base vehicle, such as lane departure systems and smart cruise control systems - Use abstraction to simplify design

## Slide 7: Describe the steps that transform a program written in a high-level language such as C into a representation that is directly executed by a computer processor.
A compiler reads the high-level source code and translates it into assembly code.
An assembler turns the program into machine code that the computer can understand.

## Slide 8: Assume a color display using 8 bits for each of the primary colors (red, green, blue) per pixel and a frame size of 1280 × 1024. a. What is the minimum size in bytes of the frame buffer to store a frame? 1280 x 1024 = 1,310,720 pixels x 3 = 3,932,160 bytes/frame b. How long would it take, at a minimum, for the frame to be sent over a 100 Mbit/s network? (3,932,160 x 8) / 100,000,000 = 0.314 seconds.

## Slide 9: Consider three different processors P1, P2, and P3 executing the same instruction set. P1 has a 3 GHz clock rate and a CPI of 1.5. P2 has a 2.5 GHz clock rate and a CPI of 1.0. P3 has a 4.0 GHz clock rate and has a CPI of 2.2. a. Which processor has the highest performance expressed in instructions per second? P2 has the highest performance at 2.5 x 109 instructions/sec. b. If the processors each execute a program in 10 seconds, find the number of cycles and the number of instructions. Cycles: Instructions: P1: 30 x 109 20 x 109 P2: 25 x 109 2.5 x 109 P3: 40 x 109 18.18 x 109 c. We are trying to reduce the execution time by 30% but this leads to an increase of 20% in the CPI. What clock rate should we have to get this time reduction? P1: 5.14 GHz P2: 4.28 GHz P3: 6.75 GHz

## Slide 10: Consider the table given next, which tracks several performance indicators for Intel desktop processors since 2010. The "Tech" column shows the minimum feature size of each processor's fabrication process. Assume that the die size has remained relatively constant and the number of transistors that comprise each processor scales at (1/ t )2, where t = the minimum feature size. For each performance indicator, calculate the average rate of improvement from 2010 to 2019, as well as the number of years required to double each at that corresponding rate.
Desktop processor | Year | Tech | Max. Clock Speed (GHz) | Integer IPC/ core | Cores | Max. DRAM Bandwidth (GB/s) | SP floating point (Gflop/s) | L3 Cache (MiB)
Westmere i7-620 | 2010 | 32 | 3.33 | 4 | 2 | 17.1 | 107 | 4
Ivy Bridge i7-3770k | 2013 | 22 | 3.90 | 6 | 4 | 25.6 | 250 | 8
Broadwell i7-6700k | 2015 | 14 | 4.20 | 8 | 4 | 34.1 | 269 | 8
Kaby Lake i7-7700k | 2017 | 14 | 4.50 | 8 | 4 | 38.4 | 288 | 8
Coffee Lake i7-9700k | 2019 | 14 | 4.90 | 8 | 8 | 42.7 | 627 | 12
Imp./year |  | % | % | % | % | % | % | %
Doubles every |  | years | years | years | years | years | years | years

## Slide 11: Consider two different implementations of the same instruction set architecture. The instructions can be divided into four classes according to their CPI (class A, B, C, and D). P1 with a clock rate of 2.5 GHz and CPIs of 1, 2, 3, and 3, and P2 with a clock rate of 3 GHz and CPIs of 2, 2, 2, and 2. Given a program with a dynamic instruction count of 1.0E6 instructions divided into classes as follows: 10% class A, 20% class B, 50% class C, and 20% class D, which implementation is faster? a. What is the global CPI for each implementation? P1: 10.4*10-4 x 2.5 x 109/106 = 2.6 P2: 6.66*10-4 x 3 x 109/106 = 2.0 b. Find the clock cycles required in both cases. P1: 2.6 x 106 P2: 2.0 x 106

## Slide 12: Compilers can have a profound impact on the performance of an application. Assume that for a program, compiler A results in a dynamic instruction count of 1.0E9 and has an execution time of 1.1 s, while compiler B results in a dynamic instruction count of 1.2E9 and an execution time of 1.5 s. a. Find the average CPI for each program given that the processor has a clock cycle time of 1 ns. Program 1: 1.1 Program 2: 1.25 b. Assume the compiled programs run on two different processors. If the execution times on the two processors are the same, how much faster is the clock of the processor running compiler A's code versus the clock of the processor running compiler B's code? It will run 1.36 times faster on compiler A vs compiler B c. A new compiler is developed that uses only 6.0E8 instructions and has an average CPI of 1.1. What is the speedup of using this new compiler versus using compiler A or B on the original processor? Compared to compiler A, the speedup is 1.66. Compared to compiler B, the speedup is 2.27.

## Slide 13: The Pentium 4 Prescott processor, released in 2004, had a clock rate of 3.6 GHz and voltage of 1.25 V. Assume that, on average, it consumed 10 W of static power and 90 W of dynamic power. The Core i5 Ivy Bridge, released in 2012, had a clock rate of 3.4 GHz and voltage of 0.9 V. Assume that, on average, it consumed 30 W of static power and 40 W of dynamic power. (a)For each processor find the average capacitive loads. CL = DP / (V2 * Freq) CL Pentium = 90 / (1.252 * 3.6) = 16 CL i5 = 40 / (0.92 * 3.4) = 16 (b)Find the percentage of the total dissipated power comprised by static power and the ratio of static power to dynamic power for each technology. Percent static power = (Static / Total) * 100 Static Pentium = (10 / (10 + 90)) * 100 = 10% Static i5 = (30 / (30 + 40)) * 100 = 42.86% Ratio Pentium = 10 / 90 = 0.111 Ratio i5 = 30/40 = 0.75 (c)If the total dissipated power is to be reduced by 10%, how much should the voltage be reduced to maintain the same leakage current? Note: power is defined as the product of voltage and current. The voltage should remain the same. P = V * C P’ = V’ * C (The current is not changing) V’ * C = V * C V’ = V

## Slide 14: Assume for arithmetic, load/store, and branch instructions, a processor has CPIs of 1, 12, and 5, respectively. Also assume that on a single processor a program requires the execution of 2.56E9 arithmetic instructions, 1.28E9 load/store instructions, and 256 million branch instructions. Assume that each processor has a 2 GHz clock frequency. Assume that, as the program is parallelized to run over multiple cores, the number of arithmetic and load/store instructions per processor is divided by 0.7 x p (where p is the number of processors) but the number of branch instructions per processor remains the same. (a)Find the total execution time for this program on 1, 2, 4, and 8 processors, and show the relative speedup of the 2, 4, and 8 processor result relative to the single processor result. 1 Processor: 9.6 seconds Relative Speed: N/A 2 Processors: 7.02 seconds Relative Speed: 1.37 4 Processors: 3.86 seconds Relative Speed: 2.49 8 Processors: 2.25 seconds Relative Speed: 4.27 (b)If the CPI of the arithmetic instructions was doubled, what would the impact be on the execution time of the program on 1, 2, 4, or 8 processors? 1 Processor: 10.88ms 2 Processors: 7.954ms 4 Processors: 4.297ms 8 Processors: 2.468ms (c)To what should the CPI of load/store instructions be reduced in order for a single processor to match the performance of four processors using the original CPI values? Reduce CPI of 25%

## Slide 15: Assume a 15 cm diameter wafer has a cost of 12, contains 84 dies, and has 0.020 defects/cm2. Assume a 20 cm diameter wafer has a cost of 15, contains 100 dies, and has 0.031 defects/cm2. (a)Find the yield for both wafers. die area = wafer area / dies per wafer yield = 1/(1 + (defects per area x die area/2))2 wafer 1 yield: 0.96 wafer 2 yield: 0.91 (b)Find the cost per die for both wafers. cost/die = Cost per wafer/(Dies per wafer x yield) wafer 1: 0.15 wafer 2: 0.16 (c)If the number of dies per wafer is increased by 10% and the defects per area unit increases by 15%, find the die area and yield new wafer1 die area = 2.10/1.1 = 1.91 cm2 new wafer1 yield = 1/(1 + 0.020 x 1.15 x 1.91/2))2 = 0.96 new wafer2 die area = 3.14/1.1 = 2.14 cm2 new wafer2 yield = 1/(1+0.031 x 1.15 x 2.14/2))2 = 0.86 (d)Assume a fabrication process improves the yield from 0.92 to 0.95. Find the defects per area unit for each version of the technology given a die area of 200 mm2. Defects per area d for 0.92 yield: 200 mm2 = 2 cm2 0.92 = 1/(1 + d x 2/2)2 = 1/(1 + d)2 (1+d)2 = 1/0.92 1 + d = (1/0.92)0.5 d = (0.92)0.5 – 1 = 0.043